## Slide 1: Introduction
Reference Models
Notes: Video Module 1-01

## Slide 2
Overview
Objectives
  Learn and understand the design issues of networks and layered modelling
  Learn and understand the OSI Reference Model
  Learn and understand the TCP/IP Reference Model
Requirements
  (Not covered in lectures) Read Sections 1.1 and 1.2
  Read 1.3.1-.1.3.2
  Read Sections 1.4.1-1.4.3
  Read Sections 1.6.2-1.6.3

## Slide 3: Introduction
Definition of a network
Key principles
  Peer to peer layers communication using a protocol
  Service between adjacent layers
Read Sections 1.1 and 1.2 (Not covered by lectures)
Read Sections 1.3.1 and 1.3.2

## Slide 4: Introduction
A network is a set of independent devices which can communicate.
How independent?
  Vendor independent
  Hardware independent
  OS independent
  …..

## Slide 5: Network Software : Issues to tackle
Error detection, error correction
Routing
Addressing, naming
Scalability
Flow control
Congestion control
Confidentiality, authentication

## Slide 6: Networking Is a Complex Problem  Divide and Conquer..
Communication should be broken in layers such that:
  Each layer has a well defined function
  Adjacent layers have neat interfaces
  Adjacent layers exchange minimal information
  Each layer hides details from upper layers

## Slide 7: Key Principles of Layered Design!
To communicate, peers must
  “speak” only to peers(they are snobs!)
  use a common language/set of rules (Protocol)
Different levels of communications (Layers)
  Above layer requests service from lower (adjacent) layer
  Lower layer provides service to above layer
  Requests/services are made/provided through interfaces.
Interface
Interface
Sender/Receiver
Sender/Receiver
Requests
Provides

## Slide 8: Decomposing Communication in Layers
International effort led by ISO (International Standards Organization)  OSI Reference Model
  Economical conflicting interests
  Result: no viable stack implementation, but a nice formal model good for education and networking experts communication
  Neat definition of:
    Functions at each layer
    Interfaces between adjacent layers
Early Internet community (mostly academia/Industry)  TCP/IP model
  Today’s Internet uses the TCP/IP model : widely implemented

## Slide 9: The OSI Reference Model
The OSI Reference Model
Read Introduction Section 1.4
Read Section 1.4.1
Notes: Video Module 1-02

## Slide 10: OSI Reference Model
Application
Application
Presentation
Presentation
Interface
Interface
Session
Session
Interface
Interface
Transport
Transport
Interface
Interface
Protocol
Protocol
Protocol
Protocol
Interface
Interface
Interface
Interface
Network
Network
Data Link
Interface
Interface
Phys.
Phys
Interface
Interface
Interface
Interface
Phys.
Phys
Network
Network
User/Client
User/Server
Data Link
Data Link
Data Link

## Slide 11: How Does Peer to Peer Communication Work?
Encapsulation (Sending)
Client/Server

## Slide 12: How Does Peer to Peer Communication Work?
Encapsulation (Sending)
Client/Server

## Slide 13: How Does Peer to Peer Communication Work?
Decapsulation (Receiving)
Client/Server

## Slide 14: How Does Peer to Peer Communication Work?
Decapsulation (Receiving)
Client/Server

## Slide 15: Two Kinds of Layers
End-to-end layers (or protocols):
  Application
  Presentation
  Session
  Transport
Point-to-point layers (or protocols):
  Network
  Link
  Physical
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 16: Implications
End-to-end layers: implemented (active) only on the end points of a conversation.
Point-to-point: implemented (active) throughout ALL the path, on endpoint nodes and intermediary nodes
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 17: End to End Layers
Application
Presentation
Session
Transport
End to end layers
(Re)-Read Section 1.4.1
Notes: Video Module 1-03

## Slide 18: Application Layer
End to end layer
It provides specialized services such as:
  DNS
  File transfer
  Email
  http
  ssh
Application
Presentation
Session
Transport
Notes: The application layer can use communication for different things. DNS provides the IP address without direct use.

## Slide 19: Presentation Layer
End to end
The two communicating entities may be different (different vendors, different OS, different CPUs)
Application
System M1
Application
System M2
Presentation
Communication System
Presentation
M1 Representation
M2 Representation
COMMON Representation
COMMON Representation
Translation
Translation
Application
Presentation
Session
Transport
Notes: Data is not represented the same way. Communication system uses network bit order. Whatever is on the wire is in network bit order.
M1 is showing something common as does M2, then goes to what the machine wants.

## Slide 20: Presentation Layer (Cont’d): Examples of Common Rep’s
Integers Representation
  Little endian (stores first the least significant byte at the address)
  Big endian (Network Byte Order) (stores first the most significant byte at the address)
  Imagine a sender that uses little endian. It wants to send a word 0x1234 to a machine that uses big endian. The receiving machine will read 0x3412
  Receiving a short number: use ntohs() before storing
  Sending a short number: use htons() before sending
  Receiving a long number: use ntohl() before storing
  Sending a long number: use htonl() before sending
Real numbers:
  Floating point numbers: IEEE 754
Application
Presentation
Session
Transport
Notes: Receiving would used network-to-host. (s) = (receiving)short. (l) = (receiving)long. Functions are on the host machine. Machines in little endian HAVE to switch. Standard for Real.

## Slide 21: Session Layer
End to end layer
Allows establishing communication sessions:
  File transfers under bad network conditions.
  Optimize the use of a communication system

## Slide 22: Transport Layer
End to end layer
Hides/adapts defects and limitations of the network sys:
  error control, addressing, congestion control, flow control….
Protocol examples: TCP, UDP
Upper Layers
1
2
3
4
5
Transport Layer
Network System
(may loose, duplicate, reorder)
Upper Layers
1
5
3
Transport Layer
4
3
Too big message
Application
Presentation
Session
Transport
Notes: Transport layer’s job is to push back the big message to the boss in the right order. It will also use flow control for slow machines. It will pace the sender. The network itself can be congested.

## Slide 23: Point to Point Layers
Network
Data Link
Physical
Point to point layers
(Re)-Read Section 1.4.1
Notes: Video Module 1-04

## Slide 24: Network Layer
Point to point layer
  Addressing
  Routing
  Congestion control (Maybe)
  Administration

## Slide 25: Data Link Layer
Point to point layer, has two sublayers:
  Logical Link Sublayer
    Framing
    Error control
    Flow control
    addressing
  Medium Access Control Sublayer

## Slide 26: Physical Layer
Transmission of raw bits
Deals with:
  Electrical specs
  Mechanical specs

## Slide 27: Conclusion
The OSI reference model is a nice conceptual model
There is no large scale implementation of an OSI protocol stack
The OSI model is largely used by networking people (conceptually).
It is good for teaching networking
Notes: Request for Comments(RFC)

## Slide 28: TCP/IP Model
TCP/IP Model versus OSI Reference Model
TCP/IP Model
Read Section 1.4.2
Notes: Video Module 1-05

## Slide 29: Difference OSI and TCP/IP Models

## Slide 30: Difference OSI and TCP/IP Models

## Slide 31: TCP/IP Model
“Running code and some consensus”
RFCs (Request For Comments)
Physical Layer
DSL
802.3
802.11
Link Layer
DSL
802.3
802.11
Network Layer
IP (and some “helpers”)
Transport Layer
TCP
UDP
Application Layer
SMTP
FTP
HTTP
DNS
Telnet
..
TCP/IP Model

## Slide 32: TCP/IP Stack
Application layer:
  SMTP: Simple Mail Transfer Protocol (Port 25)
  FTP : File Transfer Protocol (Port 20/21)
  Telnet : Terminal… (Port 23)
  HTTP: HyperText Transfer Protocol (Port 80)
  DNS : Domain Name System (port 53)
Transport layer:
  UDP: User Datagram Protocol (Protocol # 17)
  TCP: Transmission Control P. (Protocol # 6)
Network layer:
  IPv4 or IPv6 : Internet Protocol

## Slide 33: Reference Model for This Course
Physical
Link
Network
Transport
Application
Notes: WHOOAAAAAA !!!!!!!!

## Slide 34: Network Devices and Layers
Repeater (hub)
Bridges
(Data Link) Switches (or L2-switches)
Routers (or L3-switches)
Internet hosts:
  Clients
  Servers
Notes: Video Module 1-06
Making connections between physical links
All 7 layers need to be active

## Slide 35: Repeater (Hub)
Used to “repeat” a signal:
  It amplifies it
  It “Straightens” it
Physical

## Slide 36: Bridges
Old devices
  “Extends” a local area network
  Filters traffic (from subnet to another)
Data Link
Physical

## Slide 37: (Data Link)/ L2 Switches
Used on local area networks
Better than broadcast medium:
  Increases the number of simultaneous communications
Data Link
Physical

## Slide 38: Routers (or L3-Switches)
Connect different networks
Forward packets from a network to another
Network
Data Link
Physical
Notes: Routers connect networks, it will see something on one network(I saw this on that network, where should it go?)

## Slide 39: Hub, L2-switches, and Routers

## Slide 40: Hosts (Clients or Servers)
Used on end points of conversations
Network
Data Link
Physical
Application
Presentation
Session
Transport
Notes: Need all layers.

## Slide 41: Wrap Up
  Learn and understand the design issues of networks and layered modelling
  Learn and understand the OSI Reference Model
  Learn and understand the TCP/IP Reference Model
Notes: Video Module 1-07

## Slide 42: Self Study Quiz
What is a protocol?
Why is layering good? What is the role of a layer (in general)?
What are the layers in the OSI reference model?
Which layers in the OSI reference model are end-to-end?
Which layers in the OSI reference model are point-to-point?
How do end-to-end layers from point-to-point layers?
Can an end-to-end layer be implemented on an intermediary node such as a switch or a router?
On Slide 3 (Set 1), we listed some issues (services/functions): error detection, error correction, routing, addressing, naming, flow control, congestion control. For each layer in the OSI reference model, cite the issues/functions/services handled by that layer. (some issues/functions/services may be handled by different layers)
For each layer of the OSI reference model, cite one protocol used at that layer.
To which layer does the little/big endian belong in the OSI refrence model?
Which layers handle multiple similar issues/functions/services? Why do such different layers handle similar functions? Isn’t this redundant?
Cite four protocols used at the Application layer in the TCP/IP stack.
Cite two protocols used at the transport layer in the TCP/IP stack.
Cite one protocol used the network layer in the TCP/IP stack.
Does TCP provide service to IP or the reverse?

## Slide 43: Self Study Questions
What is the difference between a point-to-point layer and an end-to-end layer?
In the OSI reference model, which layers are point-to-point?
In the OSI reference model, which layers are end-to-end?
In the TCP/IP reference model, which layers are end-to-end?
Cite two transport layer protocols used on a TCP/IP network stack.
What are the services that TCP offers?
What are the services that UDP offers?
What are the services that IP offers?
What are the key differences between TCP and UDP?
Which of TCP and UDP is best?
What is the IP of the device on which you are doing this SS quiz?
What is the use of an IP address?
How many bits does an IPv4 address contain?
How many bits does an IPv4 address contain?
What is the use of a port number? How many bits does it have?
How do an IP address and a port number differ?